## Slide 1
ORDINARY HIGH WATER MARK OF THE MISSOURI RIVER BED
April 17, 2018

## Slide 2: OUTLINE
  Introductions
  Review project understanding and approach
  OHWM definition
  Data sources and compilation
  OHWM delineation methodology
  Results
  Questions

## Slide 3: INDUSTRIAL COMMISSION Department of Mineral Resources
1,000+
clients
1 focus:
YOU
  Lynn Helms - Director
  Edward Murphy – State Geologist

## Slide 4: WENCK ASSOCIATES, INC.
Who is Wenck?
1,000+
clients
www.wenck.com
Employee-owned engineering and consulting firm.
Established in 1985.
275+ Employees.
13 offices.
Project team members present
  Joel Toso – Project Manager
  Dan Ackerman
  Luke Toso

## Slide 5: RINKE NOONAN LAW FIRM
  North Dakota Government Clients
  Bottineau County Water Resource District
  Foster County Water Resource District
  Wells County Water Resource District
  Environmental Compliance & Permitting
  Clean Water Act (U.S. Army Corps)
  Food Security Act of 1985, as amended (USDA – NRCS)
  National Wildlife Refuge System (U.S. Fish & Wildlife Service)
  N.D.C.C. chs. 61-32 & 61-16.1
  Midwest Practice (ND, SD, MN, IA)
  Watershed Districts and Drainage Districts
  Public Drainage Authorities
  Water Management Litigation
Government & Water Law
Who is Rinke Noonan?
Celebrating 50 years.
  28 Attorneys & 60 Staff
  Upper Midwest Leading Law Firm in Water Law.
Water Law Attorneys
  Kale Van Bruggen
  John Kolb
  Jerry Von Korff

## Slide 6: PROJECT SCOPE AND PURPOSE
  OHWM analysis of historic Missouri River bed under what is now Lake Sakakawea.
  Initiated by State Legislation for reviewing the delineation of state-owned land.
  Presumptive determination is the US Army Corps of Engineers (USACE) survey.
  Goal – Determine if clear and convincing evidence is present that the USACE survey does not accurately represent the OHWM of the historic Missouri riverbed per state law.

## Slide 7: OHWM DEFINITION
  Based on State case law:
  The OHWM is the point at which the presence of action of the water is so continuous as to destroy the value of the land for agricultural purposes, including hay lands.

## Slide 8: OHWM DEFINITION
  Based on State case law:
  Occurs “at the level where significant, major, and substantial terrestrial vegetation ends or ceases to grow.”
  Accretions presumed to be above the OHWM and are not sovereign.
  Low-lying flat lands where the OHWM impracticable to determine due to inconclusive aerial photography or vegetation analysis is presumed above OHWM.

## Slide 9: PROJECT AREA

## Slide 10: SCOPE OF WORK
  Data gathering
  Data analysis
  Presentation of findings
  Publication of findings
  Comment review and final recommendations

## Slide 11: DATA COMPILATION
  State provided data – digital copies of aerial photography, USACE survey, and topography.
  USACE – historical records (appraisal documents) at Riverdale office, cross sections and details from Omaha office.
  USGS – flow records.
  Research case law.

## Slide 12: LEGAL RESEARCH – State Case Law
  Existing law focuses on delineating the OHWM of current waterbodies.
  Aerial photographs can provide evidence of the change in land characteristic.
  ACCRETIONS: to be sovereign, accretions must be from natural causes and on the bank of the river above the OHWM.
  Lack of cropping history or hay harvest that is more than intermittent frequency.
  Soil types or classifications that are unusable for any productive purpose.
  Vertical changes in elevation coupled with a change from wetland to terrestrial vegetation.

## Slide 13: LEGAL RESEARCH
  CLEAR & CONVINCING STANDARD
  61-33.1-03(1) directs that the presumed OHWM is the Army Corps survey completed for surface rights acquisition and supplemental plats created by the branch of cadstral survey of the BLM.
  61-33.1-03(3) – the review must determine whether clear and convincing evidence establishes that a portion of the Corps survey does not reasonably reflect the OHWM of the historical Missouri riverbed channel under state law.

## Slide 14: LEGAL RESEARCH
  CLEAR & CONVINCING STANDARD (continued)
  Clear & convincing evidence – the evidence must be such that the trier of fact is reasonably satisfied with the facts the evidence tends to prove as to be led to a firm belief or conviction. Zundel v. Zundel, 278 N.W.2d 123, 130 (N.D. 1979).
  The “clear & convincing evidence” requires less evidence than that required to meet the standard of “beyond a reasonable doubt.” Id.

## Slide 15: DATA ANALYSIS
  Analyze Corps survey data with river flow data, hydraulic model, geo-referenced aerial photography, topography, and identify discrepancies.
  Document areas where clear and convincing evidence exists based on OHWM definition and legal interpretation.

## Slide 16: DATA PROCESSING
  Geo-referencing aerial photography.
  Geo-referencing improvements of the USACE survey.
  Modeling river elevations for frequent flood events (USGS flow data and USACE cross sections).

## Slide 17: USGS FLOWS (PRE-DAM)

## Slide 18
USACE CROSS SECTIONS AND HYDRAULIC MODELING

## Slide 19: DELINEATION METHODOLOGY
  Topographic information with flow levels from modeling.
  Aerial photo interpretation.
  Appraisal documents.

## Slide 20: Data Analysis
  ***insert Jordan’s graphics here

## Slide 21
1816.0
1815.2
1815.2

## Slide 22: USACE CROSS SECTION 1613.6

## Slide 23: Data Analysis
  ***insert Jordan’s graphics here

## Slide 24: Data Analysis
  ***insert Jordan’s graphics here

## Slide 26: TABLE 2 RESULTS

## Slide 27: Data Analysis
  ***insert Jordan’s graphics here
From Figure 4 of report.
All of the NESW is below the OHWM.
There is 1.1 acres less below the OHWM in the SWSE.

## Slide 28: Data Analysis
  ***insert Jordan’s graphics here
From Figure 5 of report.
The SENW does not intersect the USACE survey.
It does in the current delineation.

## Slide 29: Data Analysis
  ***insert Jordan’s graphics here
From Figure 6 of report.

## Slide 30: Data Analysis
  ***insert Jordan’s graphics here
From Figure 7 of report.
The NENE intersects the USACE, but not the current delineation.

## Slide 31: OVERALL RESULTS
USACE OHWM | 16,687 acres
Project OHWM | 27,089 acres
Total increase in OHWM | 10,402 acres
Total increase in OHWM | 162%
(from River Mile 1482 to 1553.5).

## Slide 32: NEXT STEPS
  Publication of the findings - The report and supporting information to be made available to the public through a link on the DMR website.
  60 day public comment period.
  Public hearing (~June 26).
  Address comments and provide recommendations to Commission.

## Slide 33: QUESTIONS?